## Slide 1: Edge Detection
N. Ravitha Rajalakshmi

## Slide 2: Edge Detection
Find most relevant edges in the image.
These edges should be connected into meaningful lines and boundaries resulting in segmented image containing two (or) more regions.
The segmented results can be used for tasks such as object counting, feature extraction and classification.

## Slide 3: Basic Concepts
Edge represent boundary between two regions with different characteristics according to gray level, color (or) texture.
Derivatives can be a better operator to detect the points corresponding to edge
Given an one dimensional function f(x) , its first order and second order derivative can be expressed as the difference between two adjacent pixels.

## Slide 4: Computing derivative in an image
Since derivative is a linear operator , it can be computed using masks
For example, the following mask can be used to determine the second order derivative
0 | 0 | 0
-1 | 2 | -1
0 | 0 | 0

## Slide 5: Detection of isolated point
Second order derivative is very sensitive to sudden changes
Hence, can be used to detect an isolated point
Laplacian operator provides the second order derivative over a two dimensional function

## Slide 6: Contd..
Decide a threshold T
In the resulting filter response, those pixels whose value is larger than T can be considered as an isolated point.
0 | -1 | 0
-1 | 4 | -1
0 | -1 | 0

## Slide 7: Line detection
Second order derivative can be used to detect lines
Another variant of Laplacian operator is shown below. It is isotropic, uniform in all directions.
Using Laplacian creates double edges
-1 | -1 | -1
-1 | 8 | -1
-1 | -1 | -1

## Slide 8: Double edge effect
Original Image and Its Laplacian Response
Double edge effect is attributed to the
fact that second order derivates creates
two responses for every edge indicating the
Pixels that are occurring on the either side
of the edge pixel.

## Slide 9: Line Masks
To detect lines in specific directions, use masks that would emphasize a certain direction and be less sensitive to other directions. Popular line masks are shown below

## Slide 10: Edge Types
Three types of edge types which occurs in an image include
  Step edge – Transition of intensity level is over 1 pixel only in ideal, or few pixels on a more practical use
  Ramp edge – A slow and graduate transition
  Roof edge – Transition is back and forth into varying intensity levels

## Slide 11: Edge Profile and its derivatives of ramp edge
First derivative
  Magnitude can be used to detect the presence of edge at a certain point
  Produces thick edges
Second derivative
  Provide very strong response to fine details and noise
  Sign determine whether edge pixel lie on the dark side (or) bright side.
  Zero crossing between the negative and positive peaks of second order derivative can be used to detect the centre of thick edges

## Slide 12: Edge Model Sensitivity
Edges are highly sensitive to noise.
Hence, it is a common practice to apply
noise reduction techniques before edge detection.

## Slide 13: Basic Edge Detection Algorithm
It is a three stage process which involves
  Smoothen the image for removing noise
  Detect edge pixels
  Combine them to form meaningful edge boundaries.

## Slide 14: Edge Detection - Basics
Gradient is the tool used to find edge strength and direction at any given location (x,y) of an image.
Magnitude of gradient
Value of rate of change in the intensity
Direction of gradient
Gradient is always perpendicular
to edge direction.

## Slide 15: Prewitt and Sobel Operator
First order derivative operator centered around a pixel
It prevents the computation of the gradient at every pixel position via approximation over computation

## Slide 16: Prewitt and Sobel Operator Characteristic
Both the operator mask coefficients sum to zero and also provide a response of zero in areas of constant intensity.
Sobel Provides noise suppression as it amplifies the center pixel values
Both filters are isotropic (provides uniform result across horizontal and vertical edges.)

## Slide 17: Advanced Edge Detectors
Marr-Hildreth
  Intensity changes are not independent of image scale
  Hence the detector must be tuned to any scale
  Used an operator Laplacian of Gaussian
Gaussian Operator
Laplacian of Gaussian Operator

## Slide 18: Contd..
Gaussian and Laplacian operator can be applied separately
Gaussian reduces noise (intensity structures less than
Laplacian detect the edges
Generic Algorithm:
Filter image using Gaussian
Detect edges using Laplacian
Find zero crossings to detect the center of the edge

## Slide 19: Advanced Edge Detectors
Canny Edge Detector
  Smooth the image using Gaussian Filter
  Detect the edges using gradient
  For each detected edge (Let M(x,y) indicate the magnitude indicate the direction of detected edge pixels), perform non maximal suppression. Here, k denote the neighborhood.

## Slide 20: Contd..
  Hysteresis thresholding is performed to reduce the false edges
    Two thresholds are used.
    Create two thresholded images using (weak pixels) and using (strong pixels)
    Scan the image and mark all pixels as unvisited
    For each edge pixel x in ,
      Scan the image and mark the pixels that are connected to x as valid
    Set all unmarked pixels in as 0
    Return +
Those weak pixels that are connected to strong pixels are considered as edge pixels

## Slide 21: Edge Linking
These edge pixels from previous module result in fragmented edges.
So the method is usually followed by linking algorithm designed to assemble edge pixels into meaningful edges.
Two methods include
  Local Processing
    Pixels which are similar according to predefined criteria are linked.
  Global Processing (Hough Transform)
    Detect all pixels that lie on particular shape

## Slide 22: Local Processing – Edge Linking
Compute the gradient magnitude and direction of the input image
Construct a binary image
A denotes specified direction denotes band of acceptable directions about A
Scan rows in g(x,y) and fill in the gaps that do not exceed specified length K
To detect the gaps along other directions, rotate the image by angle and repeat step 3

## Slide 23: Global Processing – Edge Linking
Given that pixels lie on a straight line, it can be detected using Hough Transform
It utilizes parameter space for detection of line from the available edge pixels
Provided that (x1,y1) and (x2,y2) are edge pixels, there is inherently a line connecting them which needs to be detected by Hough transform

## Slide 24
a
b
Parameter space
Line equation can be expressed as
Y = a x + b
Here a and b corresponds to parameter space, they determine the slope and intercept of a line in the cartesian plane
In a deterministic parameter space, check whether the (x,y) passes through the line specified by a and b. There are multiple values of (a, b) denoting set of lines in which (x,y) passes through
If there are two edge pixels say (x1,y1) and (x2,y2) lie on the same line in cartesian plane, then they intersect in parameter space at some point
x1,y1
x2,y2
and indicate the slope and intercept of the line on which the point (x1,y1) and (x2,y2) passes through in the cartesian plane

## Slide 25
Since approaches infinity in the vertical direction, normal representation of the line is used.
Here, denotes the distance between line and origin and denote the angle between the distance vector and positive x axis
Each line in xy plane is transformed into sinusoidal in plane as shown below

## Slide 26: Hough Transform Implementation
Divide the into discrete sections (They are known as accumulator cells) and initialize its corresponding value to zero.
For an edge pixel (xi,yi) , compute i for every possible
Increase the value in the accumulator ( )
Inspect the accumulator cells with high values to identify the ’ ’