## Slide 1: 3D Face Recognition
Ravitha N

## Slide 2: Agenda
Acquisition
Preprocessing
Recognition
Why 3D recognition?
Invariant to pose and illumination variations
Facilitate detection in unconstrained manner
What is 3D image
Captures the depth information about the
Surface of the object
How 3D images are stored?
Vector format
Different file formats used?
PLY, WRL

## Slide 3: Acquisition
Passive - 3D reconstruction from 2D face images
  Shape from X (X refers to 2D characteristics such as shading, texture)
    Accuracy is less (not dense)
  Model based approaches
    More Computational Time
Active – Uses ranging scanners
(Structured Pattern Projection)
Proper Illumination is required

## Slide 4
Active Approaches
Structured Light
Time of Flight
Distorted 2D Images enable Geometrical Reconstruction
Interference between projection source and
ambient light is minimized

## Slide 5: Preprocessing and normalization
Output of the sensor is noisy (exhibit holes)
Normalization involves repositioning of the face in a particular pose
[Tech 1] Sensor Noise Processing
Median filter is used
  Order the points of neighbourhood based
  On depth
  Replace it with median value if it is an
  outlier

## Slide 6
[Tech 2] Processing of holes
  Occurs due to the absorption of the light onto the surface (pupils, eyebrows, beard)
  Holes can be filled through interpolation techniques
[Tech 3] Localization of Anthropometric Landmarks
  Locating tip of nose, corners of nose , mouth and eyes
  Used for Validation and normalization
  (i) Gaussian and Mean Curvature
    Uses partial derivatives along the surface
    Compute gaussian and mean curvature with respect to the neighborhood of 25 mm

## Slide 7
 | K<0 | K=0 | K>0
H<0 | Hyperbola | Convex Cylinder | Convex Ellipse
H=0 | Hyperbola | Plane | 
H>0 | Hyperbola | Concave Cylinder | Concave Ellipse
Use the table , to classify region
To locate nose , concave region to be identified
To locate eyes, convex region to be identified
From the set of points identified, the representative point is selected based on the maximum gaussian curvature

## Slide 8
Symmetry Plane Localization
  Exploit face symmetry to locate ridge of nose
  Extract profile signatures from depth image by rotations ()
  Profile signature obtained by intersection of rotated image with background
  By Comparing profile signature captured at and , nose point is detected.
Linear Shape and Appearance Models
  Use of statistical models
Multidecision
  Uses Gabor filter decomposition to amplify curvature
  Uses horizontal and vertical line with maximum positive curvature to obtain nose tip candidates
  Uses iterative closest point (ICP) over the candidates (Compares with average shape of nose)

## Slide 9: Face Recognition
Global
  Sensitive to Facial Expression
  Require accurate normalization step
Local
  Proper detection of key points
  Ex: Point Signature
  Robust to facial expression
Hybrid
  Effective compared to both Global and Local
  Ex: Multiple region based matching

## Slide 10: Face Recognition using local Features
Multi scale LBP depth map
Depth map at varying depths (scales) are compared
LBP is used for feature representation
It encodes the difference between the target pixel and its neighbors as one byte information
Here, extended LBP is used for high level discrimnation

## Slide 11
5 | 9 | 1
4 | 4 | 6
7 | 2 | 3
1 | 5 | -3
0 | 4 | 2
3 | -2 | -1
1
1
0
1
0
0
1
1
0
1
0
0
0
0
0
0
0
0
1
1
0
1
1
0
1
1
1
0
1
0
1
0
1
5
-3
2
-1
-2
3
0

## Slide 12
Use SIFT to extract key points
Use Constraint to limit the interaction of
Key points at different region
(i) Facial Component
(ii) Configuration Component
ORB(Oriented FAST and Rotated BRIEF)